## Slide 1: Raspberry Pi Computer Vision
Lecturer: Reza Arjmandi
Summer 2016
Preface:
Computer vision (CV) allows your Raspberry Pi to see things. In practical terms, this means that your Raspberry Pi can analyze an image, looking for items of interest and even recognizing faces and text.

## Slide 2
Installing the Raspberry Pi Camera Module
You want to use the Raspberry Pi camera module
The Raspberry Pi camera module (following Figure) is attached to a Raspberry Pi by a ribbon cable.

## Slide 3
Installing the Raspberry Pi Camera Module
This cable attaches to a special connector just behind the Ethernet socket. To fit it, pull up the levers on either side of the connector, so that they unlock, and then press the cable into the slot with the connector pads of the cable facing away from the Ethernet socket. Press the two levers of the connector back down to lock the cable in place ( following Figure).

## Slide 4
Installing the Raspberry Pi Camera Module
NOTE: The camera module packaging states that it is sensitive to static. So, before handling it, ground yourself by touching something grounded like the metal case of a PC.
The camera module requires some software configuration. The easiest way to configure it is to use raspi_config . To run raspi-config, enter the following command into a Terminal session.
$ sudo raspi-config
You will then see a list of options like those shown in following Figure

## Slide 5
Installing the Raspberry Pi Camera Module
If the option Camera is not in the list, then you need to update the operating system by running the following commands in a Terminal session:
$ sudo apt-get update
$ sudo apt-get upgrade
You need an Internet connection to do this. The second of these commands may take a few minutes to complete. When they are complete, reboot your Raspberry Pi.
Now, when you run raspi-config you will see the option to enable the camera (following Figure).

## Slide 6
Installing the Raspberry Pi Camera Module
Two commands are available for capturing still images and videos: raspiStill and raspivid.
To capture a single still image, use the raspiStill command as shown here:
$ raspistill -o image1.jpg
A preview screen displays for about five seconds and then takes a photograph and stores it in the file image1.jpg in the current directory.
To capture video, use the command raspivid:
$ raspivid -o video.h264 -t 10000
The number on the end is the recording duration in milliseconds—in this case, 10 seconds.
Both raspstill and raspivid have a large number of options. If you type either command without any parameters, help text displays options that are available.
An alternative to the camera module is to use a USB webcam

## Slide 7
Installing OpenCV
To install Opecv, first install the prerequisite packages using these commands:
    $ sudo pip install numpy
    $ sudo apt-get install python-opencv
Install
Download latest release of python library and copy python dynamic library(cv2.pyd) to following directory:
    $ sudo cp cv2.pyd /usr/local/lib/python2.7/site-packages

## Slide 8
Installing OpenCV (Raspberry Pi)
To install Opecv, first install the prerequisite packages using these commands:
    $ sudo pip install numpy
    $ sudo apt-get install python-opencv

## Slide 9
Installing SimpleCV
    OpenCV (Open Source Computer Vision Library) is released under a BSD license and hence it’s free for both academic and commercial use. It has C++, C, Python and Java interfaces and supports Windows, Linux, Mac OS, iOS and Android. OpenCV was designed for computational efficiency and with a strong focus on real-time applications. Written in optimized C/C++, the library can take advantage of multi-core processing. Enabled with OpenCL, it can take advantage of the hardware acceleration of the underlying heterogeneous compute platform.
    Computer vision is both processor- and memory-intensive, so OpenCV will work on an older Raspberry Pi, it can be frustratingly slow on anything earlier than a Raspberry Pi 3 or 2.

## Slide 10
Setting Up a USB Camera for Computer Vision
    Use a USB webcam that is compatible with the Raspberry Pi (see http://elinux.org/ RPi_USB_Webcams). Choose a good quality camera, and if you are working on a project where you need the camera close to the subject, select one that has a manual focus option. For getting really close to the subject, a low-cost USB endoscope can be useful.

## Slide 11
Using a Raspberry Pi Camera Module for Computer Vision
    You want to use a Raspberry Pi Camera Module that connects directly to your Raspberry Pi with OpenCV.
    The Raspberry Pi Camera Module does not automatically show up as a camera device. The easiest way to make the module work with OpenCV is to use the picamera Python module to capture an image with the camera.

## Slide 12
Using a Raspberry Pi Camera Module for Computer Vision
    The following class will use picamera to grab a frame from raspberry pi camera module
    from picamera import PiCamera
    from picamera.array import PiRGBArray
    from PIL import Image
    import numpy
    import cv2
    class CaptureDeviceRPiCamera:
    def __init__(self, frameSize, frameRate):
    camera = PiCamera()
    camera.resolution = frameSize
    camera.framerate = frameRate
    self.rawCapture = PiRGBArray(camera, size=frameSize)
    self.bufferIter = camera.capture_continuous(self.rawCapture, format="bgr", use_video_port=True)

## Slide 13
Using a Raspberry Pi Camera Module for Computer Vision
    def GrabFrame(self, gray):
    mat = self.bufferIter.next().array
    self.rawCapture.truncate(0)
    if(not gray):
    return mat
    return cv2.cvtColor(mat, cv2.COLOR_BGR2GRAY)

## Slide 14
CaptureDevice Class for grabing frame from Image, Video or Webcam source
    The following class will use opencv to grame a frame from image, video or webcam source for image processing
    import cv2
    class CaptureDevice:
    def __init__(self, mode, address):
    self.inputMode = mode
    self.addressFile = address
    if(mode == "-v"):
    self.cap = cv2.VideoCapture(address)
    if(mode == "-w"):
    self.cap = cv2.VideoCapture(0)

## Slide 15
CaptureDevice Class for grabing frame from Image, Video or Webcam source
    def GrabFrame(self, gray):
    if(self.inputMode == "-i"):
    if(not gray):
    return cv2.imread(self.addressFile)
    return cv2.imread(self.addressFile, 0)
    elif(self.inputMode == "-v" or self.inputMode == "-w"):
    if(self.inputMode == "-v"):
    if(not self.cap.isOpened()):
    return
    ret, frame = self.cap.read()
    if(not gray):
    return frame
    gray = cv2.cvtColor(frame, cv2.COLOR_BGR2GRAY)
    return gray

## Slide 16
Counting_Coins Project

## Slide 17
Counting_Coins Project
    import cv2
    import numpy as np
    import sys
    import CaptureDevice
    try:
    import cv2.cv as cv
    except: pass
    def CountCoins(img, cimg):
    circles = None
    try:
    circles = cv2.HoughCircles(img, cv2.HOUGH_GRADIENT, 1, 20,
    param1=50, param2=30, minRadius=0, maxRadius=0)
    except:
    circles = cv2.HoughCircles(img, cv.CV_HOUGH_GRADIENT, 1, 20, param1=50, param2=30, minRadius=0, maxRadius=0)

## Slide 18
Counting_Coins Project
    if(circles == None):
    return
    circles = np.uint16(np.around(circles))
    for i in circles[0, :]:
    # draw the outer circle
    cv2.circle(cimg, (i[0], i[1]), i[2], (0, 255, 0), 2)
    # draw the center of the circle
    cv2.circle(cimg, (i[0], i[1]), 2, (0, 0, 255), 3)
    if __name__ == "__main__":
    captureDevice = CaptureDevice.CaptureDevice(sys.argv[1], sys.argv[2])
    while(True):
    img = captureDevice.GrabFrame(True)
    img = cv2.medianBlur(img, 5)
    cimg = cv2.cvtColor(img, cv2.COLOR_GRAY2BGR)
    CountCoins(img, cimg)
    cv2.imshow('detected circles',cimg)
    if (cv2.waitKey(1) and 0xFF == ord('q')):
    break
    cv2.destroyAllWindows()

## Slide 19
Face_And_Eye_Detection Project

## Slide 20
Face_And_Eye_Detection Project
    import cv2
    import CaptureDevice
    import sys
    faceCascade = cv2.CascadeClassifier('haarcascade_frontalface_default.xml')
    eyeCascade = cv2.CascadeClassifier('haarcascade_eye.xml')
    def DetectFacesAndEyes(mat):
    gray = cv2.cvtColor(mat, cv2.COLOR_BGR2GRAY)
    faces = faceCascade.detectMultiScale(gray, 1.3, 5)
    for (x, y, w, h) in faces:
    cv2.rectangle(mat, (x, y), (x + w, y + h), (255, 0, 0), 2)
    roiGray = gray[y:y + h, x:x + w]
    roiColor = mat[y:y + h, x:x + w]
    eyes = eyeCascade.detectMultiScale(roiGray)
    for (ex, ey, ew, eh) in eyes:
    cv2.rectangle(roiColor, (ex, ey), (ex + ew, ey + eh), (0, 255, 0), 2)

## Slide 21
Face_And_Eye_Detection Project
    if __name__ == "__main__":
    device = CaptureDevice.CaptureDevice(sys.argv[1], sys.argv[2])
    while(True):
    frame = device.GrabFrame(False)
    DetectFacesAndEyes(frame)
    cv2.imshow('frame', frame)
    if(cv2.waitKey(1) and 0xFF == ord('q')):
    break
    cv2.destroyAllWindows()

## Slide 22
Face Password Project

## Slide 23
Face Password Project
    import picamera
    import time
    from SimpleCV import Color, Image, np
    import RPi.GPIO as GPIO
    quality = 400
    minMatch = 0.3
    RedLED = 18
    GreenLED = 23
    YellowLED = 24
    try:
    password = Image("password.jpg")
    except:
    password = None
    mode = "unsaved“
    saved = False
    minDist = 0.25

## Slide 24
Face Password Project
    GPIO.setmode(GPIO.BCM)
    GPIO.setup(RedLED, GPIO.OUT)
    GPIO.setup(GreenLED, GPIO.OUT)
    GPIO.setup(YellowLED, GPIO.OUT)
    with picamera.PiCamera() as camera:
    while True:
    camera.start_preview()
    time.sleep(10)
    camera.capture('pifacepw.jpg')
    image=Image("pifacepw.jpg")
    camera.stop_preview()
    faces = image.findHaarFeatures("face.xml")
    if faces:
    if not password:
    faces.draw()
    face = faces[-1]
    password = face.crop().save("password.jpg")
    print "First Run Application"
    print "Exit Program"
    break

## Slide 25
Face Password Project
else:
faces.draw()
face = faces[-1]
template = face.crop()
template.save("passwordmatch.jpg")
template = Image("passwordmatch.jpg")
diff = template.resize(password.width, password.height) - password;
#keypoints = password.findKeypointMatch(template, quality, minDist, minMatch)
if diff.findBlobs(minsize = 1000):
print "Face not matched"
print "Danger"
GPIO.output(GreenLED, 0)
GPIO.output(RedLED, 1)
GPIO.output(YellowLED, 0)
else:
print "your face detected and matched"
print "Welcome to Application"
GPIO.output(GreenLED, 1)
GPIO.output(RedLED, 0)
GPIO.output(YellowLED, 0)

## Slide 26
Face Password Project
else:
print "No face found"
print "Please look at the camera"
GPIO.output(GreenLED, 0)
GPIO.output(RedLED, 0)
GPIO.output(YellowLED, 1)

## Slide 27
Motion Detection
    Use SimpleCV to detect changes between successive frames from the camera. The program below compares each captured image with the previous image. It then detects any blobs (areas of similar color) in the difference image and if there are any larger than MIN_BLOB_SIZE, it prints out a message saying that movement was detected.
    from SimpleCV import *
    MIN_BLOB_SIZE = 1000
    c = Camera()
    old_image = c.getImage()
    while True:
      new_image = c.getImage()
      diff = new_image - old_image
      blobs = diff.findBlobs(minsize=MIN_BLOB_SIZE)
      if blobs :
        print("Movement detected")
      old_image = new_imag
    Successive frames of the image might look like following figure. When the first image is subtracted from the first, the resulting image will look like next Figure. Running blob detection on it will result in the outlined blobs shown in Next Figure.

## Slide 28
Motion Detection

## Slide 29
Motion Detection

## Slide 30
Optical Character Recognition
    Use the tesseract Optical Character Recognition (OCR) software to extract text from the image.
    To install tesseract, run the following commands:
    $ sudo apt-get install python-distutils-extra tesseract-ocr tesseract-ocr-eng
    libopencv-dev libtesseract-dev libleptonica-dev python-all-dev swig libcv-dev python-opencv python-numpy python-setuptools build-essential subversion
    $ sudo apt-get install tesseract-ocr-eng tesseract-ocr-dev libleptonica-dev
    python-all-dev swig libcv-dev
    $ sudo svn checkout
    http://python-tesseract.googlecode.com/svn/python-tesseract-0.7.4/
    $ cd python-tesseract-0.7.4
    $ sudo python setup.py build
    $ sudo python setup.py install

## Slide 31
Optical Character Recognition
    To try out tesseract, you will need an image file that contains some text.
    $ tesseract ocr_example.png found
    Tesseract Open Source OCR Engine v3.02 with Leptonica
    $ more found.txt
    The quick brown fox jumped over
    the lazy dogs back.
    $
    The tesseract library will work with most image types, including PDF, PNG, and JPG files.
    For more information on the tesseract library, see https://github.com/tesseract-ocr/ tesseract/wiki/TrainingTesseract.

## Slide 32
Contact us
www.e-system.ir
Info@e-system.ir